## Slide 1
Data Communications
Lecture 9

## Slide 2: DATA RATE LIMITS
How fast we can send data, in bits per second, over a channel.
Two theoretical formulas were developed to calculate the data rate:
Nyquist for a noiseless channel Shannon for a noisy channel.

## Slide 3
Noiseless Channel: Nyquist Rate
For a noiseless channel, the Nyquist bit rate formula defines the theoretical maximum bit rate.

## Slide 4: Noisy Channel: Shannon Capacity
In reality, we cannot have a noiseless channel; the channel is always noisy. In 1944, Claude Shannon introduced a formula, called the Shannon capacity, to determine the theoretical highest data rate for a noisy channel:

## Slide 5: Ex
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000 Hz (300 to 3300 Hz) assigned for data communications. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
ample
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 6
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as
ample
Ex

## Slide 7
Using Both Limits
In practice, we need to use both methods to find the limits and signal levels.

## Slide 8: Ex
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps. Then we use the Nyquist formula to find the number of signal levels.
ample

## Slide 9
PERFORMANCE
One important issue in Data Communications is the performance of the network— how good is it?

## Slide 10: Bandwidth
One characteristic that measures network performance
can be used in two different contexts with two different measuring values:
bandwidth in hertz bandwidth in bits per second

## Slide 11
Throughput
a measure of how fast we can actually send data through a network.

## Slide 12: Throughput
The latency or delay defines how long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source.
We can say that latency is made of four components: propagation time, transmission time, queuing time and processing delay.

## Slide 13: Examp
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
le
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 14: Ex
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be
2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
= 12,000km/ 2.4 × 108 m/s
=50ms
ample
The example shows that a bit can reach destination in only 50 ms if there is a direct cable between the source
and the destination.

## Slide 15: Ex
What are the propagation time and the transmission time for a 2.5-KB (kilobyte) message if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission time as
ample
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time.
3.53