## Slide 1
Data Communications
Lecture 16

## Slide 2: Quantization and encoding of a sampled signal

## Slide 3: Quantization and encoding of a sampled signal

## Slide 4: Quantization and encoding of a sampled signal

## Slide 5: Quantization and encoding of a sampled signal

## Slide 6: Quantization and encoding of a sampled signal

## Slide 8
It can be proven that the contribution of the quantization error to the SNR dB of the signal depends on the number of quantization levels L, or the bits per sample nb as shown in the following formula:
SNR dB =6.02nb + 1.76 dB

## Slide 9: Example
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:

## Slide 10: Example
What is the Nyquist sampling rate for each of the following signals?
a. A low-pass signal with bandwidth of 200 KHz?
b. A band-pass signal with bandwidth of 200 KHz if the lowest frequency is 100 KHz?
We have sampled a low-pass signal with a bandwidth of200 KHz using 1024 levels of quantization.
Calculate the bit rate of the digitized signal.
Calculate the SNRdB for this signal.
Calculate the PCM bandwidth of this signal.
What is the maximum data rate of a channel with a bandwidth of 200 KHz if we use four levels of digital signaling.
An analog signal has a bandwidth of 20 KHz. If we sample this signal and send it through a 30 Kbps channel what is the SNRdB?

## Slide 11: Analog Transmission

## Slide 12: DIGITAL-TO-ANALOG CONVERSION
- the process of changing one of the characteristics of an analog signal based on the information in digital data.

## Slide 13: Types of digital to analog conversion

## Slide 14
Digital-to-analog conversion
- Figure shows the relationship between the digital information, the digital-to-analog modulating process, and the resultant analog signal.

## Slide 15: Amplitude Shift Keying
In amplitude shift keying, the amplitude of the carrier signal is varied to create signal elements.
Both frequency and phase remain constant while the amplitude changes.

## Slide 16: Binary amplitude shift keying

## Slide 17: Frequency Shift Keying
In frequency shift keying, the frequency of the carrier signal is varied to represent data.
Both peak amplitude and phase remain constant for all signal elements.

## Slide 18: Binary frequency shift keying

## Slide 19: Phase Shift Keying
In phase shift keying, the phase of the carrier is varied to represent two or more different signal elements.
Both peak amplitude and frequency remain constant as the phase changes.
Today, PSK is more common than ASK or FSK.

## Slide 20: Binary phase shift keying

## Slide 21
ANALOG-TO-ANALOG CONVERSION
Analog-to-analog conversion, or analog modulation, is the representation of analog information by an analog signal.
Analog-to-analog conversion can be accomplished in three ways: AM FM and PM.

## Slide 22: Types of analog-to-analog modulation

## Slide 23: Amplitude modulation

## Slide 24: Frequency modulation

## Slide 25: Phase modulation