## Slide 1
Data Communications
Lecture 21

## Slide 2: Recap..
QAM FORMATS & BIT RATES COMPARISON |  | 
MODULATION | BITS PER SYMBOL | SYMBOL RATE
ASK/BPSK | 1 | 1 x bit rate
4QAM | 2 | 1/2 bit rate
8QAM | 3 | 1/3 bit rate
16QAM | 4 | 1/4 bit rate
32QAM | 5 | 1/5 bit rate
64QAM | 6 | 1/6 bit rate

## Slide 3
Numerical on Digital Modulation Schemes

## Slide 4
4-QAM scheme carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.

## Slide 6
4-QAM scheme carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.
Solution
In this case, r = 4, S = 1000, and N is unknown. We can find the value of N from

## Slide 7
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud. How many data elements are carried by each signal element? How many signal elements do we need?

## Slide 8
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud. How many data elements are carried by each signal element? How many signal elements do we need?
Solution
In this example, S = 1000, N = 8000, and r and L are unknown. We find first the value of r and then the value of L.

## Slide 9
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using ASK with d = 1?

## Slide 10: Bandwidth of ASK
The bandwidth B of ASK is proportional to the signal rate S.
B = (1+d)S
“d” is due to modulation and filtering, lies between 0 and 1.

## Slide 11
Binary amplitude shift keying

## Slide 13
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using ASK with d = 1?
Solution
The middle of the bandwidth is located at 250 kHz. This means that our carrier frequency can be at fc = 250 kHz. We can use the formula for bandwidth to find the bit rate (with d = 1 and r = 1).

## Slide 14
Example 5.5
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulated our data by using FSK with d = 1?

## Slide 15: Frequency Shift Keying
The digital data stream changes the frequency of the carrier signal, fc.
For example, a “1” could be represented by f1=fc +f, and a “0” could be represented by f2=fc-f.

## Slide 16
Binary frequency shift keying

## Slide 17: Bandwidth of FSK
If the difference between the two frequencies (f1 and f2) is 2f, then the required BW B will be:
B = (1+d)xS +2f