## Slide 1
Data Communications
Lecture 22

## Slide 2: Frequency Shift Keying
The digital data stream changes the frequency of the carrier signal, fc.
For example, a “1” could be represented by f1=fc +f, and a “0” could be represented by f2=fc-f.

## Slide 3
Binary frequency shift keying

## Slide 4: Bandwidth of FSK
If the difference between the two frequencies (f1 and f2) is 2f, then the required BW B will be:
B = (1+d)xS +2f

## Slide 5
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using BPSK with d = 1?

## Slide 7
Example 5.5
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulated our data by using FSK with d = 1?
Solution
This problem is similar to Example of ASK, but we are modulating by using FSK. The midpoint of the band is at 250 kHz. We choose 2Δf to be 50 kHz; this means

## Slide 8: Phase Shift Keyeing
We vary the phase shift of the carrier signal to represent digital data.
The bandwidth requirement, B is:
B = (1+d)xS
PSK is much more robust than ASK as it is not that vulnerable to noise, which changes amplitude of the signal.

## Slide 9
Example 5.3
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using BPSK with d = 1?
Solution
The middle of the bandwidth is located at 250 kHz. This means that our carrier frequency can be at fc = 250 kHz. We can use the formula for bandwidth to find the bit rate (with d = 1 and r = 1).

## Slide 10: QPSK

## Slide 12: Multi level FSK
Similarly to ASK, FSK can use multiple bits per signal element.
That means we need to provision for multiple frequencies, each one to represent a group of data bits.

## Slide 13
Example
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.
Solution
We can have L = 23 = 8. The baud rate is S = 3 Mbps/3 = 1 Mbaud. This means that the carrier frequencies must be 1 MHz apart (2Δf = 1 MHz). The bandwidth is B = 8 × 1M = 8M. Figure 5.8 shows the allocation of frequencies and bandwidth.

## Slide 14
Bandwidth of MFSK used in MFSK Example