## Slide 1
Data Communications
Lecture 23

## Slide 2
Review Questions and Exercises

## Slide 3
Q: What is Modulation of a digital signal or digital-to-analog conversion process?
Ans:
The process of changing one of the characteristics of an analog signal based on the information in digital data is called digital-to-analog conversion. It is also called modulation of a digital signal.

## Slide 4: Q: Give the Examples of a digital modulation schemes.
a. ASK changes the amplitude of the carrier.
b. FSK changes the frequency of the carrier.
c. PSK changes the phase of the carrier.
d. QAM changes both the amplitude and the phase of the carrier

## Slide 5: What is Carrier ?
A carrier is a single-frequency signal that has one of its characteristics (amplitude,frequency, or phase) changed to represent the baseband signal.
Example:

## Slide 6: Which of the three analog-to-analog conversion techniques (AM, FM, or PM) is the most susceptible to noise?
the most susceptible technique is ASK because the amplitude is more affected by noise than the phase or frequency.

## Slide 7: Define constellation diagram.
A constellation diagram helps us to define the amplitude and phase of a signal element.
The diagram is useful when we are dealing with multilevel PSK, or QAM.
In a constellation diagram, a signal element type is represented as a dot. The bit or combination of bits it can carry is often written next to it. The diagram has two axes. The horizontal X axis is related to the in-phase carrier; the vertical Y axis is related to the quadrature carrier.

## Slide 8: Calculate the baud rate for the given bit rate and type of modulation.
a. 2000 bps, FSK
b. 4000 bps, ASK
c. 6000 bps, QPSK
d. 36,000 bps, 64-QAM

## Slide 9: Use the formula S = (1/r) × N, but first we need to calculate the value of r for each case.
a. r = log22 = 1 → S = (1/1) × (2000 bps) = 2000 baud
b. r = log22 = 1 → S = (1/1) × (4000 bps) = 4000 baud
c. r = log24 = 2 → S = (1/2) × (6000 bps) = 3000 baud
d. r = log264 = 6 → S = (1/6) × (36,000 bps) = 6000 baud

## Slide 10: Calculate the bit rate for the given baud rate and type of modulation. a. 1000 baud, FSK b. 1000 baud, ASK c. 1000 baud, BPSK d. 1000 baud, 16-QAM
We use the formula N = r × S, but first we need to calculate the value of r for each case.
a. r = log22 = 1 → N = (1) × (1000 bps) = 1000 bps
b. r = log22 = 1 → N = (1) × (1000 bps) = 1000 bps
c. r = log22 = 1 → N = (1) × (1000 bps) = 1000 bps
d. r = log216 = 4 → N = (4) × (1000 bps) = 4000 bps

## Slide 11: What is the number of bits per baud for the following techniques? a. ASK with four different amplitudes b. FSK with 8 different frequencies c. PSK with four different phases d. QAM with a constellation of 128 points.
We use the formula r = log2L to calculate the value of r for each case.
a. log24 = 2
b. log28 = 3
c. log24 = 2
d. log2128 = 7

## Slide 12: Draw the constellation diagram for the following: a. ASK, with peak amplitude values of 1 and 3 b. BPSK, with a peak amplitude value of2 c. QPSK, with a peak amplitude value of 3 d. 8-QAM with two different peak amplitude values, I and 3, and four different phases.