## Slide 1
Data Communications
Lecture 49

## Slide 2
An FHSS system employs a total bandwidth of Ws = 400 MHz and an individual channel bandwidth of 100 Hz. What is the minimum number of PN bits required for each frequency hop?

## Slide 3
An FHSS system employs a total bandwidth of Ws = 400 MHz and an individual channel bandwidth of 100 Hz. What is the minimum number of PN bits required for each frequency hop?
Ws = 2kWd.
Wd= total MFSK bandwidth = channel BW (each channel of Wd width)
Wd = Mfd
The total number of individual channels is: Ws/Wd = (400 MHz)/(100 Hz) = 4 × 106.
The minimum number of PN bits = log2 (4 × 106) = 22

## Slide 4
An FHSS system using MFSK with M = 4 employs 1000 different frequencies, frequencies. What is the processing gain?
Ws = 1000 fd;
Wd = 4 fd

## Slide 7
a. Period of the PN sequence is 15
b.MFSK
c. L = 2
d.M = 2L = 4
e. k = 3
f. slow FHSS
g.2k = 8